## Slide 1: Route QoS Prediction API
X Flow Research · Next G Cloud
April 2026
Presented By: Ali Iqbal

## Slide 2: Contents
1. Background & Motivation
2. API Overview
3. API Operations
4. Subscription / Event Model
5. Gap / Overlap Analysis — vs. Existing CAMARA Portfolio
6. End-to-End Architecture
7. Interaction Diagram, Emergency Vehicle Route Planning
8. User Story

## Slide 3: Background & Motivation
The Problem
Mobile devices operating along a planned route need to know in advance whether the network will sustain required QoS at each segment.
Without trajectory-aware forecasting, applications react to degradation near it occurs — critical in emergency scenarios.
Emergency services, fleet operators, and logistics providers share this need but have no operator-agnostic CAMARA northbound API.
Existing API | Covers | Does NOT Cover
QoD API | Network QoS treatment NOW | Future condition prediction
Predictive Connectivity | Region/time-frame (sandbox) | Route/trajectory orientation (potential overlap — see slide 5)
Device Location | Current/past location | Any QoS dimension
Route QoS Prediction, NEW | Trajectory-aware per-segment forecast | ← Proposed as new API; synergy with Predictive Connectivity if overlap is significant

## Slide 4: API Overview
Positioning: Proposed as a new standalone CAMARA API. Should the community identify significant overlap with the Predictive Connectivity API, this proposal is open to co-development as a trajectory-aware, route-oriented extension of that API.
API Description
Allows an application backend to submit a planned route (array of geographic waypoints) and receive a predicted QoS profile, latency, throughput, reliability, per route segment over a specified time window. Agnostic to the underlying operator implementation.
Use Cases
Emergency vehicle routing — predict connectivity before departure; trigger QoD for prioritized sessions on low-QoS segments.
Adaptive media streaming in vehicles — pre-fetch or adapt bitrate based on predicted throughput dips.
Fleet/logistics route optimization — compare QoS forecasts across alternative routes.
Drone corridor management — validate connectivity before authorizing a flight path.

## Slide 5: API Operations
Resource: /route-qos-prediction
Operation | Method | Purpose | Key Inputs | Key Outputs
Create Prediction | POST | Submit route → per-segment QoS forecast | deviceId, route[], qosMetrics, predictionHorizon | predictionId, segments[]{latencyMs, throughputMbps, reliabilityScore, confidenceLevel}
Get Prediction | GET | Retrieve a previously computed prediction | predictionId | Full prediction object (same schema as POST response)
Delete Prediction | DELETE | Cancel and release prediction resource | predictionId | HTTP 204 No Content
Resource: /route-qos-prediction/subscriptions
Operation | Method | Purpose | Key Inputs | Key Outputs
Create Subscription | POST | Subscribe to QoS forecast change events | predictionId, notificationUrl, eventTypes[] | subscriptionId, expiresAt
Delete Subscription | DELETE | Cancel an existing subscription | subscriptionId | HTTP 204 No Content

## Slide 6: Subscription / Event Model
Event Type | Trigger Description
QOS_DEGRADATION_FORECAST | Predicted QoS will fall below threshold on a route segment within the horizon window. Developer should trigger CAMARA QoD API to pre-configure the session.
QOS_RECOVERY_FORECAST | A previously degraded segment is predicted to recover. Developer may release the prioritised QoD session.
PREDICTION_EXPIRED | The prediction resource has reached its validity window and should be refreshed with a new POST request.
Sample Notification Payload (JSON)
{
"subscriptionId": "sub-abc-123",
"eventType": "QOS_DEGRADATION_FORECAST",
"segmentId": "seg-007",
"location": { "lat": 45.071, "lon": 7.682 },
"predictedLatencyMs": 180,
"confidenceLevel": 0.85,
"expectedAt": "2026-04-16T14:32:00Z"
}

## Slide 7: Gap / Overlap Analysis — vs. Existing CAMARA Portfolio
Capability | QoD API | Predictive Connectivity | Device Location | Route QoS Prediction (NEW)
Set network QoS for a session NOW | ✅ | ❌ | ❌ | ❌
Predict QoS for a geographic region | ❌ | ⚠️ Sandbox | ❌ | ❌
Predict QoS along a planned route/trajectory | ❌ | ⚠️ Overlap | ❌ | ✅ NEW
Per-segment granularity (waypoint level) | ❌ | ❌ | ❌ | ✅ NEW
Subscribe to forecast change events | ❌ | ❌ | ❌ | ✅ NEW
Device location tracking | ❌ | ❌ | ✅ | ❌
Moving / V2X device oriented | ❌ | ❌ | ❌ | ✅ NEW
Production-ready (not sandbox) | ✅ | ❌ | ✅ | TBD
✅ Covered ❌ Not covered ⚠️ Partial / Sandbox ★ If significant overlap with Predictive Connectivity is confirmed, Route QoS Prediction may be co-developed as a trajectory-aware extension rather than a standalone new API.

## Slide 8: End-to-End Architecture
Application Layer
App (Ambulance) | Fleet Operator App | Hospital Dashboard | 3rd-Party Developer App
CAMARA Northbound Interface (NBI)
Route QoS Prediction API ★ NEW | QoD API | Device Location API
Operator Exposure & Network Analytics
Exposure Gateway | NWDAF / Network Analytics | ETSI MEC V2X Info Service
Physical Network
5G RAN | Core Network | Edge Cloud (Turin PoC)

## Slide 9: Interaction Diagram — Emergency Vehicle Route Planning
[wi.CARE+ App] [CAMARA Route QoS API] [CAMARA QoD API] [Operator Exposure GW] [NWDAF / Edge Analytics]
→ POST /route-qos-prediction { route[], deviceId, qosMetrics }
→→ Query network analytics for route segments
←← Per-segment QoS data returned
← 201 Created: predictionId + segment forecast
→ POST /subscriptions { QOS_DEGRADATION_FORECAST }
← 201 Created: subscriptionId
→→ POST /sessions (QoD) — prioritise session on low-QoS segment
←← 200 OK — QoD session confirmed
← Webhook: QOS_DEGRADATION_FORECAST { segmentId, expectedAt, latencyMs }

## Slide 10: User Stories — Additional Use Cases
Use case A: Collision Risk Detection & Safe Routing for Emergency Vehicles | 
Summary | As an emergency vehicle operator, I want to query the predicted QoS along my planned route so that I can identify low-QoS segments in advance and select the safest, best-connected corridor before departure — reducing response time in dense areas or during mass events.
API Usage | 1. POST /route-qos-prediction with the planned emergency route and required QoS metrics. 2. Inspect per-segment predictions (latency, throughput, reliability) to identify degraded corridors. 3. Compare alternative route forecasts and select the segment with highest reliability score. 4. Subscribe to QOS_DEGRADATION_FORECAST events to receive alerts if the selected route degrades. 5. On degradation event, trigger CAMARA QoD API to pre-establish a prioritised session.
Acceptance Criteria | • Per-segment QoS forecast returned within 2 s for routes of up to 50 waypoints. • Confidence level included in every segment response to support route-selection decisions. • QOS_DEGRADATION_FORECAST webhook delivered within 30 s of a forecast change.
Use case B: Real-Time Remote Triage & Diagnostics | 
Summary | As an ambulance crew member, I want to query the predicted network throughput along the route to the hospital so that I can ensure sufficient bandwidth for streaming patient vitals, ECGs, and HD video — and pre-configure a prioritised session on any segment below threshold.
API Usage | 1. POST /route-qos-prediction with the ambulance route and throughput/latency QoS metrics. 2. Identify segments where predicted throughput falls below the HD-video minimum (e.g. 8 Mbps). 3. Trigger CAMARA QoD API on flagged segments before the vehicle arrives, ensuring a prioritised session. 4. Subscribe to QOS_DEGRADATION_FORECAST; switch to compressed-stream fallback if forecast worsens. 5. DELETE prediction and subscription when the ambulance reaches the hospital.
Acceptance Criteria | • Throughput and latency forecast per segment returned within 2 s of route submission. • QoD session pre-established on low-QoS segments at least 30 s before vehicle arrival. • QOS_DEGRADATION_FORECAST webhook delivered within 30 s to trigger adaptive bitrate fallback.

## Slide 11: Thank You
Thank You
ali.iqbal@xflowresearch.com